## Slide 1: Verification services
To get a cleaner chip in shorter time

## Slide 2: Stages in making a product
Characterization (with or without a client)
Architectural
Design + basic functional testing.
Producing first version.
Testing and corrections.
Making beta version.
Field testing (with client).
Final version.

## Slide 3
Changes for chip design
Characterization (with or without a client)
Architectural
Design + module testing.
Full chip integration & verification.
Random testing.(RTL freeze)
Gate level (with timing)
Final version(typeout).

## Slide 4: Testing hardware modules
DUT.v
Design Under Test
inputs
outputs
SIGNAL DRIVER
Simulate the full system inputs to our DUT
OUTPUTS CHECKER
Checks the DUT outputs against the DUT expected outputs
PASS/FAIL
Message to log file
Test bench.v
(simulate board)

## Slide 5: Problems with the old hardware testing method
The signal driver machine only worked in low level. We had to prepare the data manually to feed it to the machine. Making high level sequences is very hard.
The machine was relevant to the test-bench. Making it harder to reuse.
We had to prepare the test outcome to match with the DUT outputs. We don’t have an automatic mechanism to prepare it for us from the inputs. So it is very hard to do random tests.

## Slide 6: Automatic hardware verification environment
DUT.v
Design Under Test
inputs
outputs
SIGNAL DRIVER
Generate the input signals to our DUT
SEQUENCE DRIVER
INPUT
MONITOR
OUTPUT
MONITOR
CHECKER
(S/B)
Message to log file
SEQUENCE
LIBRARY
The Checker (score board). Prepare form the input signals, the expected output signals. Compare them and give a pass/fail massage.
The sequence driver. Send the scenarios to the design.
Signal Driver. Translate the high level scenarios (sequences) to low level signal, to be driven to the DUT.
The monitors (inputs & outputs). Read back the input/output signals and generate back a data structure to be transfer to the checker.
Active/Passive

## Slide 7
Changes for chip design
Characterization (with or without a client)
Architectural
Design + module testing.
Full chip verification.
Random testing.
Gate level (with timing)
Final version.

## Slide 8: Full chip integration
DUT2.v
DUT1.v
DUT0.v
Full chip
inputs
Full chip
outputs
The chip integrator integrate all the chip’s modules into the chip’s top level file.
Most modules inputs are now being driven by the previous modules (except for the chips inputs).
Configuration
inputs

## Slide 9: Full chip verification environment
The verification full chip integrator should combine all the module’s environments into one big full chip environment.
The modules which have inputs that are driven by other modules outputs, don’t need theirs sequence & signals drivers anymore. So we just need to turn them off (passive mode)
The score board will see no different because it gets it’s input from the input monitor which is still on.
DUT2.v
MON
MON
SB
SEQ
Driver
DUT1.v
MON
MON
SEQ
Driver
DUT0.v
MON
MON
SB
SEQ
Driver
Passive
Active
Full chip
inputs
Full chip
outputs
Configure driver
Cnf
SEQ
SB

## Slide 10: Full chip verification tests
DUT2.v
MON
MON
SB
SEQ
Driver
DUT1.v
MON
MON
SB
SEQ
Driver
DUT0.v
MON
MON
SB
SEQ
Driver
Passive
Active
VIRTUAL
SEQUENCE DRIVER
Full chip
inputs
Full chip
outputs
The first sequence driver will generate it’s sequences from it’s library. To control this sequence driver we add a virtual sequence driver that give it it’s sequences.
Configure driver
Cnf
SEQ

## Slide 11
Changes for chip design
Characterization (with or without a client)
Architectural
Design + module testing.
Full chip verification.
Random testing.
Gate level (with timing)
Final version.

## Slide 12: Random testing
DUT2.v
MON
MON
SB
SEQ
Driver
DUT1.v
MON
MON
SB
SEQ
Driver
DUT0.v
MON
MON
SB
SEQ
Driver
VIRTUAL
SEQUENCE DRIVER
Full chip
inputs
Full chip
outputs
Because we have only one shot we can not take the chance we have miss something on out test plan. So after the test plan tests had passed we run random tests to generate scenarios that we didn’t thought of initially.
Also we keep developing the environment to have more easy pass/fail tests. For …
Configure driver
Cnf
SEQ
Top level score board

## Slide 13
Changes for chip design
Characterization (with or without a client)
Architectural
Design + module testing.
Full chip verification.
Random testing.
Gate level (with timing)
Final version.

## Slide 14: Gate level
DUT2.v
DUT1.v
DUT0.v
Full chip
inputs
Full chip
outputs
After the code is checked (for some stability) we do synthesis. This turn the code lines into electronic gates & flip-flops
Some of the inner signals will be lost in the process.
D
Q
CLK
rst
D
Q
CLK
rst

## Slide 15: Gate level testing
MON
MON
SB
SEQ
Driver
DUT1.v
MON
MON
SB
SEQ
Driver
DUT0.v
MON
MON
SB
SEQ
Driver
VIRTUAL
SEQUENCE DRIVER
Full chip
inputs
Full chip
outputs
Because will lost some of the inner signals we can’t work with all of the monitors & score boards. But we now knew that those tests had passed in logic so if they fail now it is an electrical problem.
D
Q
CLK
rst
D
Q
CLK
rst
Configure driver
Cnf
SEQ
Top level score board

## Slide 16: Gate level with timing
Up till now we looked at the signals as rising & falling in 0 time. In the real would they don’t.
clock
input
output
clock
input
output
In real life it takes the gates & flip-flops to change their values.

## Slide 17: Gate level with timing
So we have to make sure that all the inputs will be ready ‘setup time’ before the clock and remain stable for ‘hold time’ after the clock.
Our flip-flop takes ‘clock to Q’ time to produce it’s output. And this output may be the input for the next level.
And out logic has also ‘delay time’ to work.
As we can see in gate level with timing simulation all the signals are being pushed forward and we need to make sure that the gate level tests still pass.
clock
input
output
Setup time
Hold time
Clock to Q time

## Slide 18
And …
Type out
We send the design to production and hope for the best 